## Slide 1
NETWORK HEALTH MONITORING SYSTEM
Computer Networks Laboratory CSE20110
Mini-project presentation
Computer Networks Laboratory (CSE20110)
Department of Computer Engineering and Technology
Presented by:
Shreyash Kumbhar – 1262250001
Mansi Gunjal – 1262250002
Tanvi Newase – 1262250003
Shruti Pitale - 1262252214
Group: 6 Panel: E Batch: E1
Faculty: Swati
Academic Year: 2026–2027
Date: 21-10-2026

## Slide 2
Problem and Objectives
Computer Networks Laboratory CSE20110
Problem
In a network with multiple devices, checking each IP manually is slow and inconvenient.
Without one view, it is difficult to notice unreachable devices, high latency and packet loss.
Objectives
1. Check reachability of configured devices using ICMP ping.
2. Measure latency, packet loss and UP/DOWN status.
3. Show results, health alerts and simulated device statistics on one dashboard.

## Slide 3
Proposed Design and Tools
Computer Networks Laboratory CSE20110
CONFIGURED IPs (devices.json)
↓
ICMP PING TEST (monitor.py)
↓
FLASK BACKEND (app.py)
↙ ↘
SNMP-LIKE DATA ALERT RULES
(simulated values) (threshold checks)
↘ ↙
WEB DASHBOARD (dashboard.html)
Tools: Python, Flask, HTML/CSS, JSON, Windows ping
Protocols: ICMP for connectivity; HTTP for local dashboard
Targets: Google DNS, Cloudflare DNS, localhost, test IP
Dashboard URL: http://127.0.0.1:5000/

## Slide 4
Implementation and Working
Computer Networks Laboratory CSE20110
STEP 1 Read device names and IPs from devices.json
↓
STEP 2 Send 5 ICMP pings to each IP (monitor.py)
↓
STEP 3 Extract average latency and packet-loss %
↓
STEP 4 Mark UP (<100% loss) or DOWN (100% loss)
↓
STEP 5 Add simulated CPU, memory, interface and uptime
↓
STEP 6 Generate alerts and render the Flask dashboard
app.py:- Starts Flask, combines monitoring data, checks alert limits.
monitor.py:- Runs ping and calculates reachability, latency and loss.
snmp_simulator.py:- Generates sample device statistics (not real SNMP).
qos.py:- Contains GOOD / MODERATE / WARNING / POOR / CRITICAL rules; needs to be called from app.py to display QoS.
Dashboard refreshes automatically every 10 seconds.

## Slide 5
Testing and Results
Computer Networks Laboratory CSE20110
WHAT THE DASHBOARD CHECKS
• 127.0.0.1: local loopback connectivity
• 8.8.8.8 and 1.1.1.1: external network reachability
• 192.0.2.1: example address for unreachable-device testing
• Alerts: device DOWN, loss >10%, latency >100 ms, high simulated CPU/memory or interface DOWN
Input: Four IP addresses configured in devices.json
Displayed: Device status, latency, loss, SNMP-like values and alerts
Validation: Compare dashboard ping values with terminal ping output
Note: Actual results vary by network; ICMP may be blocked.

## Slide 6
Working Demonstration
Computer Networks Laboratory CSE20110
Function to demonstrate
Demonstrate ICMP device reachability and dashboard alerts.
1. Open project folder in VS Code.
2. Run py app.py in the terminal.
3. Visit http://127.0.0.1:5000/.
4. Show UP/DOWN, latency, loss, SNMP-like values and alerts.
5. Explain the automatic 10-second refresh.
Success criterion: Dashboard loads and shows measured ping results for configured IPs.

## Slide 7
Conclusion and Contributions
Computer Networks Laboratory CSE20110
Outcome: A working local dashboard for basic network reachability and health monitoring.
Concepts used: ICMP Echo, RTT, packet loss, HTTP and alert thresholds.
Limitation: SNMP-like CPU, memory, interface and uptime values are simulated.
Future work: Add real SNMP polling, history graphs and notifications.
Key learning: How Python collects ping results and Flask displays network status in a browser.
Team Contributions:-
Shreyash Kumbhar : Dashboard design using HTML and CSS.
Mansi Gunjal : Network monitoring using ICMP Ping.
Tanvi Newase : Flask backend and alert generation.
Shruti Pitale: SNMP simulation and QoS analysis.

## Slide 8
References
Computer Networks Laboratory CSE20110
[1] J. Postel, “Internet Control Message Protocol,” RFC 792, September 1981. https://www.rfc-editor.org/rfc/rfc792
[2] D. Harrington, R. Presuhn, and B. Wijnen, “An Architecture for Describing SNMP Management Frameworks,” RFC 3411, December 2002. https://www.rfc-editor.org/rfc/rfc3411
[3] Pallets Projects, “Flask Documentation — Quickstart.” https://flask.palletsprojects.com/en/stable/quickstart/